# Lab 3 Report
The purpose of this lab is to solidify you to the usage of some important lab equipments. This lab will allow you to learn about short circuits, voltage source, a breadboard, a multimeter.
## Component List
- 5 x 1kOhm Resistor
- 2 x 10kOhm Resistor
- 1 x 4.7kOhm Resistor
- 1 x 2.2kOhm Resistor
- 1 x 1.5kOhm Resistor
## Useful Equations
"Error%" = {{Calculated-Measured} over Calculated} * 100
## Experiment 1

Figure 1: Circuit diagram of Experiment 1.
### Components and Instruments used:
- A computer: used in the pre-lab to get experiment details from the Moodle
- Resistor kit: contains the resistors to create circuits in the breadboard
- Tektronix PS280 power supply: voltage source
- Fluke multimeter: used to get measurements such as potential difference, current, etc.
- Breadboard: used to create circuits and connect wires to find values
### Procedure:
1. Create the circuit shown in Figure 1 on breadboard using the shown resistor values.
2. Connect the power supply and set it to the 12V of DC voltage.
3. Set the multimeter to voltage measurement mode and for each resistor, connect the multimeter as parallel to the resistors and measure the voltage drops.
4. Set the multimeter to current measurement mode and for each resistor, connect the multimeter as series before or after to the resistor that you want to measure the current passing through.
### Results
RESULTS WITHOUT UNITS WILL NOT BE GRADED!
Table 1: Voltage measurements.
VARIABLE	CALCULATED	MEASURED	ERROR%
VR1		12V
VR2		12V
VR3		6V
VR4		6V
VR5		0V

Table 2: Current measurements.
VARIABLE	CALCULATED	MEASURED	ERROR%
IR1		8mA
IR2		5.45mA
IR3		6mA
IR4		6mA
IR5		0mA

## Experiment 2 – Voltage Divider

Figure 2: Circuit diagram of Experiment 2.
### Components and Instruments used:
- A computer: used in the pre-lab to get experiment details from the Moodle
- Resistor kit: contains the resistors to create circuits in the breadboard
- Tektronix PS280 power supply: current source
- Fluke multimeter: used to get measurements such as potential difference, current, etc.
- Breadboard: used to create circuits and connect wires to find values
### Procedure:
1. Create the circuit shown in Figure 2 on breadboard using the shown resistor values.
2. Connect the power supply in constant voltage mode and set the voltage to 9V.
3. Set the multimeter to voltage measurement mode and for each resistor, connect the multimeter as parallel to the resistors and measure the voltage drops.
4. Set the multimeter to current measurement mode and for each resistor, connect the multimeter as series before or after to the resistor that you want to measure the current passing through.
5. Compare the resistor ratios R1, R2, and R3 to potential difference over load R4 and R5. Verify that the potential difference over R3 and 9V is proportional to the R2 and R1.
### Results
RESULTS WITHOUT UNITS WILL NOT BE GRADED!
Table 3: Voltage measurements.
VARIABLE	CALCULATED	MEASURED	ERROR%
VR1		3.46V
VR2		2.90V
VR3		2.64V
VR4		5.54V
VR5		2.64V

Table 4: Current measurements.
VARIABLE	CALCULATED	MEASURED	ERROR%
IR1		3.45mA
IR2		2.9mA
IR3		2.62mA
IR4		0.57mA
IR5		0.23mA

Table 5: Voltage dividing results for R4.
RATIO	THEORIC VR4 W/O LOAD	MEASURED VR4 W/ LOAD	ERROR%
{ R2 + R3 } over { R1 + R2 + R3 } = 0.6667	6.0003V	5.54V	7.67%

Table 6: Voltage dividing results for R5.
RATIO	THEORIC VR5 W/O LOAD	MEASURED VR5 W/ LOAD	ERROR%
{ R3 } over { R1 + R2 + R3 } = 0.3333	2.9997	2.64V	11.99%